## Slide 1: Computer Organization and Architecture Designing for Performance
11th Edition
Chapter 1
Basic Concepts and Computer Evolution

## Slide 2: Computer Architecture Computer Organization
Computer Architecture
Attributes of a system visible to the programmer
Have a direct impact on the logical execution of a program
Architectural attributes include:
Instruction set, number of bits used to represent various data types, I/O mechanisms, techniques for addressing memory
Computer Organization
The operational units and their interconnections that realize the architectural specifications
Organizational attributes include:
Hardware details transparent to the programmer, control signals, interfaces between the computer and peripherals, memory technology used
Notes: In describing computers, a distinction is often made between computer architecture
and computer organization. Although it is difficult to give precise definitions
for these terms, a consensus exists about the general areas covered by each
(e.g., see [VRAN80], [SIEW82], and [BELL78a]); an interesting alternative view
is presented in [REDD76].
Computer architecture refers to those attributes of a system visible to a
programmer or, put another way, those attributes that have a direct impact on
the logical execution of a program. A term that is often used interchangeably with computer
architecture is instruction set architecture (ISA) . The ISA defines instruction
formats, instruction opcodes, registers, instruction and data memory; the effect of
executed instructions on the registers and memory; and an algorithm for controlling
instruction execution. Computer organization refers to the operational
units and their interconnections that realize the architectural specifications.
Examples of architectural attributes include the instruction set, the number of bits
used to represent various data types (e.g., numbers, characters), I/O mechanisms,
and techniques for addressing memory. Organizational attributes include those
hardware details transparent to the programmer, such as control signals; interfaces
between the computer and peripherals; and the memory technology used.
For example, it is an architectural design issue whether a computer will have
a multiply instruction. It is an organizational issue whether that instruction will
be implemented by a special multiply unit or by a mechanism that makes repeated
use of the add unit of the system. The organizational decision may be based on the
anticipated frequency of use of the multiply instruction, the relative speed of the two
approaches, and the cost and physical size of a special multiply unit.
Historically, and still today, the distinction between architecture and organization
has been an important one. Many computer manufacturers offer a family of
computer models, all with the same architecture but with differences in organization.
Consequently, the different models in the family have different price and performance
characteristics. Furthermore, a particular architecture may span many years and
encompass a number of different computer models, its organization changing with
changing technology.

## Slide 3: IBM System 370 Architecture
IBM System/370 architecture
  Was introduced in 1970
  Included a number of models
  Could upgrade to a more expensive, faster model without having to abandon original software
  New models are introduced with improved technology, but retain the same architecture so that the customer’s software investment is protected
  Architecture has survived to this day as the architecture of IBM’s mainframe product line
Notes: A prominent example of both these phenomena is the IBM
System/370 architecture. This architecture was first introduced in 1970 and included
a number of models. The customer with modest requirements could buy a cheaper,
slower model and, if demand increased, later upgrade to a more expensive, faster
model without having to abandon software that had already been developed. Over
the years, IBM has introduced many new models with improved technology to replace
older models, offering the customer greater speed, lower cost, or both. These newer
models retained the same architecture so that the customer’s software investment was
protected. Remarkably, the System/370 architecture, with a few enhancements, has
survived to this day as the architecture of IBM’s mainframe product line.

## Slide 4: Structure and Function
Hierarchical system
  Set of interrelated subsystems
  Hierarchical nature of complex systems is essential to both their design and their description
  Designer need only deal with a particular level of the system at a time
  Concerned with structure and function at each level
Structure
  The way in which components relate to each other
Function
  The operation of individual components as part of the structure
Notes: A computer is a complex system; contemporary computers contain millions of
Elementary electronic components. How, then, can one clearly describe them?
The key is to recognize the hierarchical nature of most complex systems, including
the computer [SIMO96]. A hierarchical system is a set of interrelated subsystems,
each of the latter, in turn, hierarchical in structure until we reach some lowest level
of elementary subsystem.
The hierarchical nature of complex systems is essential to both their design
and their description. The designer need only deal with a particular level of the
system at a time. At each level, the system consists of a set of components and
their interrelationships. The behavior at each level depends only on a simplified,
abstracted characterization of the system at the next lower level. At each level, the
designer is concerned with structure and function:
• Structure: The way in which the components are interrelated.
• Function: The operation of each individual component as part of the structure.
In terms of description, we have two choices: starting at the bottom and building
up to a complete description, or beginning with a top view and decomposing the
system into its subparts. Evidence from a number of fields suggests that the top-down
approach is the clearest and most effective [WEIN75].
The approach taken in this book follows from this viewpoint. The computer
system will be described from the top down. We begin with the major components
of a computer, describing their structure and function, and proceed to successively
lower layers of the hierarchy. The remainder of this section provides a very brief
overview of this plan of attack.

## Slide 5: Function
There are four basic functions that a computer can perform:
  Data processing
    Data may take a wide variety of forms and the range of processing requirements is broad
  Data storage
    Short-term
    Long-term
  Data movement
    Input-output (I/O) - when data are received from or delivered to a device (peripheral) that is directly connected to the computer
    Data communications – when data are moved over longer distances, to or from a remote device
  Control
    A control unit manages the computer’s resources and orchestrates the performance of its functional parts in response to instructions
Notes: Both the structure and functioning of a computer are, in essence, simple. In general terms, there are
only four basic functions that a computer can perform:
Data Processing. The data may take a wide
variety of forms, and the range of processing requirements is broad. However, we
shall see that there are only a few fundamental methods or types of data processing.
Data Storage. Even if the computer is processing
data on the fly (i.e., data come in and get processed, and the results go out
immediately), the computer must temporarily store at least those pieces of data
that are being worked on at any given moment. Thus, there is at least a short-term
data storage function. Equally important, the computer performs a long-term data
storage function. Files of data are stored on the computer for subsequent retrieval
and update.
Data Movement. The computer’s operating environment consists of devices that serve as
either sources or destinations of data. When data are received from or delivered to
a device that is directly connected to the computer, the process is known as input–
output (I/O), and the device is referred to as a peripheral. When data are moved
over longer distances, to or from a remote device, the process is known as data
communications.
Control. Within the computer, a control unit manages the computer’s resources and orchestrates the
performance of its functional parts in response to those instructions.

## Slide 6: Structure
Figure 1.1 The Computer: Top-Level Structure
Notes: We now look in a general way at the internal structure of a computer. We begin with
a traditional computer with a single processor that employs a microprogrammed
control unit, then examine a typical multicore structure.
Figure 1.1 provides a hierarchical view
of the internal structure of a traditional single-processor computer.

## Slide 7: There are four main structural components of the computer:
CPU – controls the operation of the computer and performs its data processing functions
Main Memory – stores data
I/O – moves data between the computer and its external environment
System Interconnection – some mechanism that provides for communication among CPU, main memory, and I/O
Notes: There are four main structural components:
• Central processing unit (CPU): Controls the operation of the computer and
performs its data processing functions; often simply referred to as processor.
• Main memory: Stores data.
• I/O: Moves data between the computer and its external environment.
• System interconnection: Some mechanism that provides for communication
among CPU, main memory, and I/O. A common example of system interconnection
is by means of a system bus, consisting of a number of conducting
wires to which all the other components attach.

## Slide 8: CPU
Major structural components:
Control Unit
  Controls the operation of the CPU and hence the computer
  Arithmetic and Logic Unit (ALU)
  Performs the computer’s data processing function
  Registers
  Provide storage internal to the CPU
  CPU Interconnection
  Some mechanism that provides for communication among the control unit, ALU, and registers
Notes: There may be one or more of each of the aforementioned components.
Traditionally, there has been just a single processor. In recent years, there has been
increasing use of multiple processors in a single computer. Some design issues relating
to multiple processors crop up and are discussed as the text proceeds; Part Five
focuses on such computers.
Each of these components will be examined in some detail in Part Two.
However, for our purposes, the most interesting and in some ways the most complex
component is the CPU. Its major structural components are as follows:
• Control unit: Controls the operation of the CPU and hence the computer.
• Arithmetic and logic unit (ALU): Performs the computer’s data processing
functions.
• Registers: Provides storage internal to the CPU.
• CPU interconnection: Some mechanism that provides for communication
among the control unit, ALU, and registers.
Part Three covers these components, where we will see that complexity is added by
the use of parallel and pipelined organizational techniques. Finally, there are several
approaches to the implementation of the control unit; one common approach is
a microprogrammed implementation. In essence, a microprogrammed control unit
operates by executing microinstructions that define the functionality of the control
unit. With this approach, the structure of the control unit can be depicted, as in
Figure 1.1. This structure is examined in Part Four.

## Slide 9: Multicore Computer Structure
Central processing unit (CPU)
  Portion of the computer that fetches and executes instructions
  Consists of an ALU, a control unit, and registers
  Referred to as a processor in a system with a single processing unit
Core
  An individual processing unit on a processor chip
  May be equivalent in functionality to a CPU on a single-CPU system
  Specialized processing units are also referred to as cores
Processor
  A physical piece of silicon containing one or more cores
  Is the computer component that interprets and executes instructions
  Referred to as a multicore processor if it contains multiple cores
Notes: As was mentioned, contemporary
computers generally have multiple processors. When these processors all reside
on a single chip, the term multicore computer is used, and each processing unit
(consisting of a control unit, ALU, registers, and perhaps cache) is called a core . To
clarify the terminology, this text will use the following definitions.
■ Central processing unit (CPU) : That portion of a computer that fetches and
executes instructions. It consists of an ALU, a control unit, and registers. In a
system with a single processing unit, it is often simply referred to as a processor .
■ Core : An individual processing unit on a processor chip. A core may be
equivalent in functionality to a CPU on a single-CPU system. Other specialized processing units,
such as one optimized for vector and matrix operations, are also referred to as cores.
■ Processor: A physical piece of silicon containing one or more cores. The
processor is the computer component that interprets and executes instructions.
If a processor contains multiple cores, it is referred to as a multicore
processor .
After about a decade of discussion, there is broad industry consensus on this
usage.

## Slide 10: Cache Memory
Multiple layers of memory between the processor and main memory
Is smaller and faster than main memory
Used to speed up memory access by placing in the cache data from main memory that is likely to be used in the near future
A greater performance improvement may be obtained by using multiple levels of cache, with level 1 (L1) closest to the core and additional levels (L2, L3, etc.) progressively farther from the core
Notes: Another prominent feature of contemporary computers is the use of multiple
layers of memory, called cache memory , between the processor and main memory.
Chapter 4 is devoted to the topic of cache memory. For our purposes in this section,
we simply note that a cache memory is smaller and faster than main memory and is
used to speed up memory access by placing in the cache, data from main memory
that is likely to be used in the near future. A greater performance improvement may
be obtained by using multiple levels of cache, with level 1 (L1) closest to the core
and additional levels (L2, L3, and so on) progressively farther from the core. In this
scheme, level n is smaller and faster than level n + 1.

## Slide 11: Figure 1.2
Notes: Figure 1.2 is a simplified view of the principal components of a typical multicore
computer. Most computers, including embedded computers in smartphones
and tablets, plus personal computers, laptops, and workstations, are housed on a
motherboard. Before describing this arrangement, we need to define some terms.
A printed circuit board (PCB) is a rigid, flat board that holds and interconnects chips and
other electronic components. The board is made of layers, typically two to ten,
that interconnect components via copper pathways that are etched into the board.
The main printed circuit board (PCB) in a computer is called a system board or
motherboard , while smaller ones that plug into the slots in the main board are
called expansion boards.
The most prominent elements on the motherboard are the chips. A chip is
a single piece of semiconducting material, typically silicon, upon which electronic
circuits and logic gates are fabricated. The resulting product is referred to as an
integrated circuit .
The motherboard contains a slot or socket for the processor chip, which typically
contains multiple individual cores, in what is known as a multicore processor .
There are also slots for memory chips, I/O controller chips, and other key computer
components. For desktop computers, expansion slots enable the inclusion of more
components on expansion boards. Thus, a modern motherboard connects only a
few individual chip components, with each chip containing from a few thousand up
to hundreds of millions of transistors.
Figure 1.2 shows a processor chip that contains eight cores and an L3 cache.
Not shown is the logic required to control operations between the cores and the
cache and between the cores and the external circuitry on the motherboard. The
figure indicates that the L3 cache occupies two distinct portions of the chip surface.
However, typically, all cores have access to the entire L3 cache via the aforementioned
control circuits. The processor chip shown in Figure 1.2 does not represent
any specific product, but provides a general idea of how such chips are laid out.
Next, we zoom in on the structure of a single core, which occupies a portion of
the processor chip. In general terms, the functional elements of a core are:
■ Instruction logic: This includes the tasks involved in fetching instructions and
decoding each instruction to determine the instruction operation and the
memory locations of any operands.
■ Arithmetic and logic unit (ALU): Performs the operation specified by an
instruction.
■ Load/store logic: Manages the transfer of data to and from main memory via
cache.
The core also contains an L1 cache, split between an instruction cache
(I-cache) that is used for the transfer of instructions to and from main memory, and
an L1 data cache, for the transfer of operands and results. Typically, today’s processor
chips also include an L2 cache as part of the core. In many cases, this cache
is also split between instruction and data caches, although a combined, single L2
cache is also used.
Keep in mind that this representation of the layout of the core is only intended
to give a general idea of internal core structure. In a given product, the functional
elements may not be laid out as the three distinct elements shown in Figure 1.2,
especially if some or all of these functions are implemented as part of a microprogrammed
control unit.

## Slide 12: Figure 1.3 Motherboard with Two Intel Quad-Core Xeon Processors
Source: Courtesy of Chassis Plans Rugged Rackmount Computers
Notes: It will be instructive to look at some real-
world examples that illustrate the hierarchical structure of computers.
Figure 1.3 is a photograph of the
motherboard for a computer built around two Intel Quad-Core
Xeon processor chips. Many of the elements labeled on the photograph are discussed subsequently
in this book. Here, we mention the most important, in addition to the processor
sockets:
■ PCI-Express slots for a high-end
display adapter and for additional peripherals
(Section 3.6 describes PCIe).
■ Ethernet controller and Ethernet ports for network connections.
■ USB sockets for peripheral devices.
■ Serial ATA (SATA) sockets for connection to disk memory (Section 7.7
discusses Ethernet, USB, and SATA).
■ Interfaces for DDR (double data rate) main memory chips (Section 5.3
discusses DDR).
■ Intel 3420 chipset is an I/O controller for direct memory access operations
between peripheral devices and main memory (Section 7.5 discusses DDR).

## Slide 13: Figure 1.4
Notes: Following our top-down
strategy, as illustrated in Figures 1.1 and 1.2, we can
now zoom in and look at the internal structure of a processor chip, referred to as a
processor unit (PU). For variety, we look at an IBM chip instead of the Intel processor
chip. Figure 1.4 is a to-scale layout of the processor chip for the IBM z13 mainframe
computer [LASC16]. This chip has 3.99 billion transistors. The superimposed
labels indicate how the silicon surface area of the chip is allocated. We see that this
chip has eight cores, or processors. In addition, a substantial portion of the chip is
devoted to the L3 cache, which is shared by all eight cores. The L3 control logic controls
traffic between the L3 cache and the cores and between the L3 cache and the
external environment. Additionally, there is storage control (SC) logic between the
cores and the L3 cache. The memory controller (MC) function controls access to
memory external to the chip. The GX I/O bus controls the interface to the channel
adapters accessing
the I/O.

## Slide 14: Figure 1.5
Notes: Going down one level deeper, we examine the internal structure of a single
core, as shown in the photograph of Figure 1.5. The core implements the z13 instruction
set architecture, referred to as the z/Architecture. Keep in mind that this is a
portion of the silicon surface area making up a single-
processor chip. The main sub-areas
within this core area are the following:
■ ISU (instruction sequence unit): Determines the sequence in which instructions
are executed in what is referred to as a superscalar architecture. It enables
the out-of-order (OOO) pipeline. It tracks register names, OOO instruction
dependency, and handling of instruction resource dispatch. These concepts are
discussed in Chapter 16.
■ IFB (instruction fetch and branch) and ICM (instruction cache and merge)
These two subunits contain the 128-kB1 instruction cache, branch prediction
logic, instruction fetching controls, and buffers. The relative size of these subunits
is the result of the elaborate branch prediction design.
■ IDU (instruction decode unit): The IDU is fed from the IFU buffers, and is
responsible for the parsing and decoding of all z/Architecture operation codes.
■ LSU (load-store unit): The LSU contains the 96-kB L1 data cache, and manages
data traffic between the L2 data cache and the functional execution
units. It is responsible for handling all types of operand accesses of all lengths,
modes, and formats as defined in the z/Architecture.
■ XU (translation unit): This unit translates logical addresses from instructions
into physical addresses in main memory. The XU also contains a translation
lookaside buffer (TLB) used to speed up memory access. TLBs are discussed
in Chapter 8.
PC (core pervasive unit): Used for instrumentation and error collection.
■ FXU (fixed-point unit): The FXU executes fixed-point arithmetic operations.
■ VFU (vector and floating-point units): The binary floating-unit part handles
all binary and hexadecimal floating-point operations, as well as fixed-point
multiplication operations. The decimal floating-unit part handles both fixed-point
and floating-point operations on numbers that are stored as decimal
digits. The vector execution part handles vector operations.
■ RU (recovery unit): The RU keeps a copy of the complete state of the system
that includes all registers, collects hardware fault signals, and manages the
hardware recovery actions.
■ COP (dedicated co-processor): The COP is responsible for data compression
and encryption functions for each core.
are needed.
L2D: A 2-MB L2 data cache for all memory traffic other than instructions.
■ L2I: A 2-MB L2 instruction cache.

## Slide 15: History of Computers First Generation: Vacuum Tubes
Vacuum tubes were used for digital logic elements and memory
IAS computer
  Fundamental design approach was the stored program concept
    Attributed to the mathematician John von Neumann
    First publication of the idea was in 1945 for the EDVAC
  Design began at the Princeton Institute for Advanced Studies
  Completed in 1952
  Prototype of all subsequent general-purpose computers
Notes: The first generation of computers used vacuum tubes for digital logic elements and
memory. A number of research and then commercial computers were built using
vacuum tubes. For our purposes, it will be instructive to examine perhaps the most
famous first-generation computer, known as the IAS computer.
A fundamental design approach first implemented in the IAS computer is
known as the stored-program concept . This idea is usually attributed to the mathematician
John von Neumann. Alan Turing developed the idea at about the same time.
The first publication of the idea was in a 1945 proposal by von Neumann for a new
computer, the EDVAC (Electronic Discrete Variable Computer).
In 1946, von Neumann and his colleagues began the design of a new stored-
program computer, referred to as the IAS computer, at the Princeton Institute for
Advanced Studies. The IAS computer, although not completed until 1952, is the
prototype of all subsequent general-purpose computers.

## Slide 16: Figure 1.6
Notes: Figure 1.6 shows the general structure of the IAS computer (compare with Figure 1.1).
It consists of
• A main memory, which stores both data and instructions
• An arithmetic and logic unit (ALU) capable of operating on binary data
• A control unit, which interprets the instructions in memory and causes them
to be executed
• Input/output (I/O) equipment operated by the control unit
This structure was outlined in von Neumann’s earlier proposal, which is worth
quoting in part at this point [VONN45]:
2.2 First: Since the device is primarily a computer, it will
have to perform the elementary operations of arithmetic most frequently.
These are addition, subtraction, multiplication, and division.
It is therefore reasonable that it should contain specialized
organs for just these operations.
It must be observed, however, that while this principle as such
is probably sound, the specific way in which it is realized requires
close scrutiny. At any rate a central arithmetical part of the device will
probably have to exist, and this constitutes the first specific part: CA .
2.3 Second: The logical control of the device, that is, the
proper sequencing of its operations, can be most efficiently carried
out by a central control organ. If the device is to be elastic ,
that is, as nearly as possible all purpose , then a distinction must
be made between the specific instructions given for and defining
a particular problem, and the general control organs that see to it
that these instructions—no matter what they are—are
carried out. The former must be stored in some way; the latter are represented
by definite operating parts of the device. By the central control we
mean this latter function only, and the organs that perform it form
the second specific part: CC .
2.4 Third: Any device that is to carry out long and complicated
sequences of operations (specifically of calculations) must
have a considerable memory . . .
The instructions which govern a complicated problem may
constitute considerable material, particularly so, if the code is circumstantial
(which it is in most arrangements). This material must
be remembered.
At any rate, the total memory constitutes the third specific
part of the device: M.
2.6 The three specific parts CA, CC (together C), and M correspond
to the associative neurons in the human nervous system. It
remains to discuss the equivalents of the sensory or afferent and the
motor or efferent neurons. These are the input and output organs of
the device.
The device must be endowed with the ability to maintain
input and output (sensory and motor) contact with some specific
medium of this type. The medium will be called the outside recording
medium of the device: R .
2.7 Fourth: The device must have organs to transfer information
from R into its specific parts C and M. These organs form its
input , the fourth specific part: I . It will be seen that it is best to make
all transfers from R (by I) into M and never directly from C.
2.8 Fifth: The device must have organs to transfer from its
specific parts C and M into R. These organs form its output , the
fifth specific part: O . It will be seen that it is again best to make all
transfers from M (by O) into R, and never directly from C.

## Slide 17: Figure 1.7
Notes: With rare exceptions, all of today’s computers have this same general structure
and function and are thus referred to as von Neumann machines . Thus, it is worthwhile
at this point to describe briefly the operation of the IAS computer [BURK46,
GOLD54]. Following [HAYE98], the terminology and notation of von Neumann
are changed in the following to conform more closely to modern usage; the examples
accompanying this discussion are based on that latter text.
The memory of the IAS consists of 4,096 storage locations, called words , of
40 binary digits (bits) each. Both data and instructions are stored there. Numbers are
represented in binary form, and each instruction is a binary code. Figure 1.7 illustrates
these formats. Each number is represented by a sign bit and a 39-bit value. A word
may alternatively contain two 20-bit instructions, with each instruction consisting
of an 8-bit operation code (opcode ) specifying the operation to be performed and
a 12-bit address designating one of the words in memory (numbered from 0 to 999).

## Slide 18: Registers
Memory buffer register (MBR)
Contains a word to be stored in memory or sent to the I/O unit
Or is used to receive a word from memory or from the I/O unit
Memory address register (MAR)
Specifies the address in memory of the word to be written from or read into the MBR
Instruction register (IR)
Contains the 8-bit opcode instruction being executed
Instruction buffer register (IBR)
Employed to temporarily hold the right-hand instruction from a word in memory
Program counter (PC)
Contains the address of the next instruction pair to be fetched from memory
Accumulator (AC) and multiplier quotient (MQ)
Employed to temporarily hold operands and results of ALU operations
Notes: The control unit operates the IAS by fetching instructions from memory
and executing them one at a time. We explain these operations with reference to
Figure 1.6. This figure reveals that both the control unit and the ALU contain storage
locations, called registers , defined as follows:
Memory buffer register (MBR): Contains a word to be stored in memory or sent
to the I/O unit, or is used to receive a word from memory or from the I/O unit.
• Memory address register (MAR): Specifies the address in memory of the word
to be written from or read into the MBR.
• Instruction register (IR ): Contains the 8-bit opcode instruction being executed.
• Instruction buffer register (IBR): Employed to hold temporarily the right-hand
instruction from a word in memory.
• Program counter (PC): Contains the address of the next instruction pair to be
fetched from memory.
• Accumulator (AC) and multiplier quotient (MQ): Employed to hold temporarily
operands and results of ALU operations. For example, the result of
multiplying two 40-bit numbers is an 80-bit number; the most significant 40 bits
are stored in the AC and the least significant in the MQ.

## Slide 19: Figure 1.8
Notes: The IAS operates by repetitively performing an instruction cycle, as shown in
Figure 1.8. Each instruction cycle consists of two sub-cycles. During the fetch cycle,
the opcode of the next instruction is loaded into the IR and the address portion is
loaded into the MAR. This instruction may be taken from the IBR, or it can be
obtained from memory by loading a word into the MBR, and then down to the IBR,
IR, and MAR.
Why the indirection? These operations are controlled by electronic circuitry
and result in the use of data paths. To simplify the electronics, there is only one
register that is used to specify the address in memory for a read or write and only
one register used for the source or destination.
Once the opcode is in the IR, the execute cycle is performed. Control circuitry
interprets the opcode and executes the instruction by sending out the appropriate
control signals to cause data to be moved or an operation to be performed by the
ALU.
Figure 1.8 shows several examples of instruction execution by the control unit.
Note that each operation requires several steps, some of which are quite elaborate.
The multiplication operation requires 39 suboperations, one for each bit position
except that of the sign bit.

## Slide 20: Table 1.1 The IAS Instruction Set
Instruction Type | Opcode | Symbolic Representation | Description
Data transfer | 00001010 | LOAD MQ | Transfer contents of register MQ to the accumulator AC
 | 00001001 | LOAD MQ,M(X) | Transfer contents of memory location X to MQ
 | 00100001 | STOR M(X) | Transfer contents of accumulator to memory location X
 | 00000001 | LOAD M(X) | Transfer M(X) to the accumulator
 | 00000010 | LOAD –M(X) | Transfer –M(X) to the accumulator
 | 00000011 | LOAD ¦M(X)¦ | Transfer absolute value of M(X) to the accumulator
 | 00000100 | LOAD –¦M(X)¦ | Transfer –¦M(X)¦ to the accumulator
Unconditional branch | 00001101 | JUMP M(X,0:19) | Take next instruction from left half of M(X)
 | 00001110 | JUMP M(X,20:39) | Take next instruction from right half of M(X)
Conditional Branch | 00001111 | JUMP + M(X,0:19) | Take next instruction from right half of M(X)
 | 00010000 | JUMP + M(X,20:39) | If number in the accumulator is nonnegative, take next instruction from right half of M(X)
Arithmetic | 00000101 | ADD M(X) | Add M(X) to AC; put the result in AC
 | 00000111 | ADD ¦M(X)¦ | Add ¦M(X)¦ to AC; put the result in AC
 | 00000110 | SUB M(X) | Subtract M(X) from AC; put the result in AC
 | 00001000 | SUB ¦M(X)¦ | Subtract ¦M(X)¦ from AC; put the remainder in AC
 | 00001011 | MUL M(X) | Multiply M(X) by MQ; put most significant bits of result in AC, put least significant bits in MQ
 | 00001100 | DIV M(X) | Divide AC by M(X); put the quotient in MQ and the remainder in AC
 | 00010100 | LSH | Multiply accumulator by 2; that is, shift left one bit position
 | 00010101 | RSH | Divide accumulator by 2; that is, shift right one position
Address modify | 00010010 | STOR M(X,8:19) | Replace left address field at M(X) by 12 rightmost bits of AC
 | 00010011 | STOR M(X,28:39) | Replace right address field at M(X) by 12 rightmost bits of AC
(Table can be found on page 16 in the textbook.)
Notes: The IAS computer had a total of 21 instructions, which are listed in Table 1.1.
These can be grouped as follows:
• Data transfer: Move data between memory and ALU registers or between
two ALU registers.
Unconditional branch: Normally, the control unit executes instructions in
sequence from memory. This sequence can be changed by a branch instruction,
which facilitates repetitive operations.
• Conditional branch: The branch can be made dependent on a condition, thus
allowing decision points.
• Arithmetic: Operations performed by the ALU.
• Address modify: Permits addresses to be computed in the ALU and then
inserted into instructions stored in memory. This allows a program considerable
addressing flexibility.
Table 1.1 presents instructions (excluding I/O instructions)
in a symbolic, easy-to-read form. In binary form, each instruction must conform to the format of
Figure 1.7b. The opcode portion (first 8 bits) specifies which of the 21 instructions is
to be executed. The address portion (remaining 12 bits) specifies which of the 4,096
memory locations is to be involved in the execution of the instruction.

## Slide 21: Figure 1.9
Notes: The basic elements of a digital computer, as we know, must perform storage,
movement, processing, and control functions. Only two fundamental types of components
are required (Figure 1.9): gates and memory cells. A gate is a device that
implements a simple Boolean or logical function, For example, an AND gate with
inputs A and B and output C implements the expression IF A AND B ARE TRUE
THEN C IS TRUE. Such devices are called gates because they control data flow
in much the same way that canal gates control the flow of water. The memory cell
is a device that can store one bit of data; that is, the device can be in one of two
stable states at any time. By interconnecting large numbers of these fundamental
devices, we can construct a computer.

## Slide 22: Integrated Circuits
Data storage – provided by memory cells
Data processing – provided by gates
Data movement – the paths among components are used to move data from memory to memory and from memory through gates to memory
Control – the paths among components can carry control signals
A computer consists of gates, memory cells, and interconnections among these elements
The gates and memory cells are constructed of simple digital electronic components
Exploits the fact that such components as transistors, resistors, and conductors can be fabricated from a semiconductor such as silicon
Many transistors can be produced at the same time on a single wafer of silicon
Transistors can be connected with a processor metallization to form circuits
Notes: We can relate this to our four
basic functions as follows:
• Data storage: Provided by memory cells.
• Data processing: Provided by gates.
• Data movement: The paths among components are used to move data from
memory to memory and from memory through gates to memory.
• Control: The paths among components can carry control signals. For example,
a gate will have one or two data inputs plus a control signal input that activates
the gate. When the control signal is ON, the gate performs its function on the
data inputs and produces a data output. Conversely, when the control signal
is OFF, the output line is null, such as is produced by a high impedance state.
Similarly, the memory cell will store the bit that is on its input lead when the
WRITE control signal is ON and will place the bit that is in the cell on its output
lead when the READ control signal is ON.
Thus, a computer consists of gates, memory cells, and interconnections among
these elements. The gates and memory cells are, in turn, constructed of simple electronic
components, such as transistors and capacitors.
The integrated circuit exploits the fact that such components as transistors,
resistors, and conductors can be fabricated from a semiconductor such as silicon.
It is merely an extension of the solid-state art to fabricate an entire circuit in a tiny
piece of silicon rather than assemble discrete components made from separate
pieces of silicon into the same circuit. Many transistors can be produced at the same
time on a single wafer of silicon. Equally important, these transistors can be connected
with a process of metallization to form circuits.

## Slide 23: Transistors
  The fundamental building block of digital circuits used to construct processors, memories, and other digital logic devices
  Active part of the transistor is made of silicon or some other semiconductor material that can change its electrical state when pulsed
      In its normal state the material may be nonconductive or conductive
      The transistor changes its state when voltage is applied to the gate
  Discrete component
      A single, self-contained transistor
      Were manufactured separately, packaged in their own containers, and soldered or wired together onto Masonite-like circuit boards
Notes: The fundamental building block of digital circuits used to construct processors,
memories, and other digital logic devices is the transistor. The active part of the transistor
is made of silicon or some other semiconductor material that can change its
electrical state when pulsed. In its normal state, the material may be nonconductive
or conductive, either impeding or allowing current flow. When voltage is applied to
the gate, the transistor changes its state.
A single, self-contained transistor is called a discrete component . Throughout
the 1950s and early 1960s, electronic equipment was composed largely of discrete
components—transistors, resistors, capacitors, and so on. Discrete components
were manufactured separately, packaged in their own containers, and soldered
or wired together onto Masonite-like circuit boards, which were then installed in
computers, oscilloscopes, and other electronic equipment. Whenever an electronic
device called for a transistor, a little tube of metal containing a pinhead-sized piece
of silicon had to be soldered to a circuit board. The entire manufacturing process,
from transistor to circuit board, was expensive and cumbersome.
These facts of life were beginning to create problems in the computer industry.
Early second-generation computers contained about 10,000 transistors. This
figure grew to the hundreds of thousands, making the manufacture of newer, more
powerful machines increasingly difficult.

## Slide 24: Figure 1.10
Notes: Microelectronics means, literally, “small electronics.” Since the beginning of digital
electronics and the computer industry, there has been a consistent trend toward the
reduction in size of digital electronic circuits. Before examining the implications and
benefits of this trend, we need to say something about the nature of digital electronics.
A more detailed discussion is found in Chapter 12.
The integrated circuit exploits the fact that such components as transistors,
resistors, and conductors can be fabricated from a semiconductor such as silicon.
It is merely an extension of the solid-state art to fabricate an entire circuit in a tiny
piece of silicon rather than assemble discrete components made from separate
pieces of silicon into the same circuit. Many transistors can be produced at the same
time on a single wafer of silicon. Equally important, these transistors can be connected
with a process of metallization to form circuits.
Figure 1.10 depicts the key concepts in an integrated circuit. A thin wafer of
silicon is divided into a matrix of small areas, each a few millimeters square. The
identical circuit pattern is fabricated in each area, and the wafer is broken up into
chips . Each chip consists of many gates and/or memory cells plus a number of input
and output attachment points. This chip is then packaged in housing that protects
it and provides pins for attachment to devices beyond the chip. A number of these
packages can then be interconnected on a printed circuit board to produce larger
and more complex circuits.

## Slide 25: Figure 1.11
Notes: Figure 1.11a indicates what a packaged processor or
memory chip looks like, and Figure 1.11b shows a packaged chip wired onto a
motherboard.

## Slide 26: Figure 1.12
Notes: Initially, only a few gates or memory cells could be reliably manufactured
and packaged together. These early integrated circuits are referred to as small scale
Integration (SSI). As time went on, it became possible to pack more and more
Components on the same chip. This growth in density is illustrated in Figure 1.12; it is
one of the most remarkable technological trends ever recorded.
This figure reflects the
famous Moore’s law, which was propounded by Gordon Moore, cofounder of Intel,
in 1965 [MOOR65]. Moore observed that the number of transistors that could be
put on a single chip was doubling every year and correctly predicted that this pace
would continue into the near future. To the surprise of many, including Moore, the
pace continued year after year and decade after decade. The pace slowed to a doubling
every 18 months in the 1970s but has sustained that rate ever since.

## Slide 27: Moore’s Law
1965; Gordon Moore – co-founder of Intel
Observed number of transistors that could be put on a single chip was doubling every year
The pace slowed to a doubling every 18 months in the 1970’s but has sustained that rate ever since
Consequences of Moore’s law:
The cost of computer logic and memory circuitry has fallen at a dramatic rate
The electrical path length is shortened, increasing operating speed
Computer becomes smaller and is more convenient to use in a variety of environments
Reduction in power and cooling requirements
Fewer interchip connections
Notes: The consequences of Moore’s law are profound:
1. The cost of a chip has remained virtually unchanged during this period of
rapid growth in density. This means that the cost of computer logic and memory
circuitry has fallen at a dramatic rate.
2. Because logic and memory elements are placed closer together on more
densely packed chips, the electrical path length is shortened, increasing
operating speed.
3. The computer becomes smaller, making it more convenient to place in a
variety of environments.
4. There is a reduction in power and cooling requirements.
5. The interconnections on the integrated circuit are much more reliable than
solder connections. With more circuitry on each chip, there are fewer interchip
connections.

## Slide 28: Figure 1.13
Notes: The increasing requirements for denser and faster memories have led to efforts to
further compact standard packaging approaches, with one of the most important
and widely used being the multichip module. In traditional system design, each individual
process or memory chip is packaged and then wired to a motherboard (see
Figure 1.11).
The basic idea behind developing MCM technology is to decrease the average
spacing between ICs in an electronic system. An MCM is a chip package that
contains several bare chips mounted close together on a substrate (base) of some
kind and interconnected by conductors in that base. The short tracks between the
chips increase performance and eliminate much of the noise that external tracks
between individual chip packages can pick up.
MCMs are classified by substrate, which include the following types
[BLUM99]:
■ MCM-L: composed of metal traces on stacked organic laminate sheets.
■ MCM-C: metal patterned and interconnected on co-fired ceramic layers.
■ MCM-D: vapor-deposited, patterned metal layers alternating sequentially
with spun-on or vapor-deposited dielectric thin films.
The basic architecture of an MCM is composed of (Figure 1.13):
■ Integrated circuits: Bare chips mounted on/in the surface of the substrate.
■ Level-1 interconnections: Connections between chips through paths in the
substrate.
■ Substrate: The common base that provides all the signal interconnections and
the mechanical support for all chips
■ MCM package: Provides a degree of protection to the circuits in addition to
heat removal and interconnections.
■ Level-2 interconnections: Provides the necessary interface to the printed circuit
board on which the MCM is mounted.

## Slide 29: Evolution of Intel Microprocessors (1 of 4)
 | 4004 | 8008 | 8080 | 8086 | 8088
Introduced | 1971 | 1972 | 1974 | 1978 | 1979
Clock speeds | 108 kHz | 108 kHz | 2 MHz | 2 MHz, 8 MHz, 10 MHz | 5 MHz, 8 MHz
Bus width | 4 bits | 8 bits | 8 bits | 16 bits | 8 bits
Number of transistors | 2,300 | 3,500 | 6,000 | 29,000 | 29,000
Feature size (m) | 10 | 8 | 6 | 3 | 6
Addressable memory | 640 bytes | 16 KB | 64 KB | 1 MB | 1 MB
(a) 1970s Processors
Notes: Throughout this book, we rely on many concrete examples of computer design and
implementation to illustrate concepts and to illuminate trade-offs.
Numerous systems,both contemporary and historical, provide examples of important computer
architecture design features. But the book relies principally on examples from two
processor families: the Intel x86 and the ARM architectures. The current x86 offerings
represent the results of decades of design effort on complex instruction set computers
(CISCs) . The x86 incorporates the sophisticated design principles once found
only on mainframes and supercomputers and serves as an excellent example of CISC
design. An alternative approach to processor design is the reduced instruction set
computer (RISC) . The ARM architecture is used in a wide variety of embedded systems
and is one of the most powerful and best-designed RISC-based systems on the
market. In this section and the next, we provide a brief overview of these two systems.
In terms of market share, Intel has ranked as the number one maker of microprocessors
for non-embedded systems for decades, a position it seems unlikely to
yield. The evolution of its flagship microprocessor product serves as a good indicator
of the evolution of computer technology in general.
Table 1.3 shows that evolution. Interestingly, as microprocessors have grown
faster and much more complex, Intel has actually picked up the pace. Intel used
to develop microprocessors one after another, every four years. But Intel hopes
to keep rivals at bay by trimming a year or two off this development time, and has
done so with the most recent x86 generations.

## Slide 30: Evolution of Intel Microprocessors (2 of 4)
 | 80286 | 386TM DX | 386TM SX | 486TM DX CPU
Introduced | 1982 | 1985 | 1988 | 1989
Clock speeds | 6–12.5 MHz | 16–33 MHz | 16–33 MHz | 25–50 MHz
Bus width | 16 bits | 32 bits | 16 bits | 32 bits
Number of transistors | 134,000 | 275,000 | 275,000 | 1.2 million
Feature size (m) | 1.5 | 1 | 1 | 0.8–1
Addressable memory | 16 MB | 4 GB | 16 MB | 4 GB
Virtual memory | 1 GB | 64 TB | 64 TB | 64 TB
Cache | – | – | – | 8 kB
(b) 1980s Processors
Notes: Table 1.3 (continued)

## Slide 31: Evolution of Intel Microprocessors (3 of 4)
 | 486TM SX | Pentium | Pentium Pro | Pentium II
Introduced | 1991 | 1993 | 1995 | 1997
Clock speeds | 16–33 MHz | 60–166 MHz | 150–200 MHz | 200–300 MHz
Bus width | 32 bits | 32 bits | 64 bits | 64 bits
Number of transistors | 1.185 million | 3.1 million | 5.5 million | 7.5 million
Feature size (m) | 1 | 0.8 | 0.6 | 0.35
Addressable memory | 4 GB | 4 GB | 64 GB | 64 GB
Virtual memory | 64 TB | 64 TB | 64 TB | 64 TB
Cache | 8 kB | 8 kB | 512 kB L1 and 1 MB L2 | 512 kB L2
(c) 1990s Processors
Notes: Table 1.3 (continued)

## Slide 32: Evolution of Intel Microprocessors (4 of 4)
 | Pentium III | Pentium 4 | Core 2 Duo | Core i7 EE 4960X | Core i9- 7900X
Introduced | 1999 | 2000 | 2006 | 2013 | 2017
Clock speeds | 450–660 MHz | 1.3–1.8 GHz | 1.06–1.2 GHz | 4 GHz | 4.3 GHz
Bus width | 64 bits | 64 bits | 64 bits | 64 bits | 64 bits
Number of transistors | 9.5 million | 42 million | 167 million | 1.86 billion | 7.2 billion
Feature size (nm) | 250 | 180 | 65 | 22 | 14
Addressable memory | 64 GB | 64 GB | 64 GB | 64 GB | 128 GB
Virtual memory | 64 TB | 64 TB | 64 TB | 64 TB | 64 TB
Cache | 512 kB L2 | 256 kB L2 | 2 MB L2 | 1.5 MB L2/ 1.5 MB L3 | 14 MB L3
Number of cores | 1 | 1 | 2 | 6 | 10
(d) Recent Processors
Notes: Table 1.3 (continued)
Almost 40 years after its introduction in 1978, the x86 architecture continues to
dominate the processor market outside of embedded systems. Although the organization
and technology of the x86 machines have changed dramatically over the decades,
the instruction set architecture has evolved to remain backward compatible with earlier
versions. Thus, any program written on an older version of the x86 architecture
can execute on newer versions. All changes to the instruction set architecture have
involved additions to the instruction set, with no subtractions. The rate of change has
been the addition of roughly one instruction per month added to the architecture
[ANTH08], so that there are now thousands of instructions in the instruction set.
The x86 provides an excellent illustration of the advances in computer hardware
over the past 35 years. The 1978 8086 was introduced with a clock speed of
5 MHz and had 29,000 transistors. A six-core
Core i7 EE 4960X introduced in 2013
operates at 4 GHz, a speedup of a factor of 800, and has 1.86 billion transistors,
about 64,000 times as many as the 8086. Yet the Core i7 EE 4960X is in only a
slightly larger package than the 8086 and has a comparable cost.

## Slide 33: Highlights of the Evolution of the Intel Product Line: (1 of 2)
8080
World’s first general-purpose microprocessor
8-bit machine, 8-bit data path to memory
Was used in the first personal computer (Altair)
8086
A more powerful 16-bit machine
Has an instruction cache, or queue, that prefetches a few instructions before they are executed
The first appearance of the x86 architecture
The 8088 was a variant of this processor and used in IBM’s first personal computer (securing the success of Intel
80286
Extension of the 8086 enabling addressing a 16-MB memory instead of just 1MB
80386
Intel’s first 32-bit machine
First Intel processor to support multitasking
80486
Introduced the use of much more sophisticated and powerful cache technology and sophisticated instruction pipelining
Also offered a built-in math coprocessor
Notes: It is worthwhile to list some of the highlights of the evolution of the Intel product
line:
■ 8080: The world’s first general-
purpose microprocessor. This was an 8-bit
machine, with an 8-bit data path to memory. The 8080 was used in the first
personal computer, the Altair.
8086:
■ A far more powerful, 16-bit machine. In addition to a wider data path
and larger registers, the 8086 sported an instruction cache, or queue, that
prefetches a few instructions before they are executed. A variant of this processor,
the 8088, was used in IBM’s first personal computer, securing the success
of Intel. The 8086 is the first appearance of the x86 architecture.
■ 80286: This extension of the 8086 enabled addressing a 16-MB memory instead
of just 1 MB.
■ 80386: Intel’s first 32-bit machine, and a major overhaul of the product. With a
32-bit architecture, the 80386 rivaled the complexity and power of minicomputers
and mainframes introduced just a few years earlier. This was the first Intel processor
to support multitasking, meaning it could run multiple programs at the same time.
■ 80486: The 80486 introduced the use of much more sophisticated and powerful
cache technology and sophisticated instruction pipelining. The 80486 also
offered a built-in math coprocessor, offloading complex math operations from
the main CPU.

## Slide 34: Highlights of the Evolution of the Intel Product Line: (2 of 2)
Pentium
Pentium Pro
Pentium II
Pentium III
Pentium 4
Core
Core 2
Intel introduced the use of superscalar techniques, which allow multiple instructions to execute in parallel
Continued the move into superscalar organization with aggressive use of register renaming, branch prediction, data flow analysis, and speculative execution
Incorporated Intel MMX technology, which is designed specifically to process video, audio, and graphics data efficiently
Incorporated additional floating-point instructions
Streaming SIMD Extensions (SSE)
Includes additional floating-point and other enhancements for multimedia
First Intel x86 micro-core
Extends the Core architecture to 64 bits
Core 2 Quad provides four cores on a single chip
More recent Core offerings have up to 10 cores per chip
An important addition to the architecture was the Advanced Vector Extensions instruction set
Notes: ■ Pentium: With the Pentium, Intel introduced the use of superscalar techniques,
which allow multiple instructions to execute in parallel.
■ Pentium Pro: The Pentium Pro continued the move into superscalar organization
begun with the Pentium, with aggressive use of register renaming, branch
prediction, data flow analysis, and speculative execution.
■ Pentium II: The Pentium II incorporated Intel MMX technology, which is
designed specifically to process video, audio, and graphics data efficiently.
■ Pentium III: The Pentium III incorporates additional floating-
Point instructions: The Streaming SIMD Extensions (SSE) instruction set extension added
70 new instructions designed to increase performance when exactly the same
operations are to be performed on multiple data objects. Typical applications
are digital signal processing and graphics processing.
■ Pentium 4: The Pentium 4 includes additional floating-
Point and other enhancements for multimedia.
■ Core: This is the first Intel x86 microprocessor with a dual core, referring to
the implementation of two cores on a single chip.
■ Core 2: The Core 2 extends the Core architecture to 64 bits. The Core 2 Quad
provides four cores on a single chip. More recent Core offerings have up to 10
cores per chip. An important addition to the architecture was the Advanced
Vector Extensions instruction set that provided a set of 256-bit, and then 512-
bit, instructions for efficient processing of vector data.

## Slide 35: Embedded Systems
The use of electronics and software within a product
Billions of computer systems are produced each year that are embedded within larger devices
Today many devices that use electric power have an embedded computing system
Often embedded systems are tightly coupled to their environment
  This can give rise to real-time constraints imposed by the need to interact with the environment
    Constraints such as required speeds of motion, required precision of measurement, and required time durations, dictate the timing of software operations
  If multiple activities must be managed simultaneously this imposes more complex real-time constraints
Notes: The term embedded system refers to the use of electronics and software within a
product, as opposed to a general-purpose computer, such as a laptop or desktop
system. Millions of computers are sold every year, including laptops, personal
computers, workstations, servers, mainframes, and supercomputers. In contrast, billions
of computer systems are produced each year that are embedded within larger
devices. Today, many, perhaps most, devices that use electric power have an embedded
computing system. It is likely that in the near future virtually all such devices
will have embedded computing systems.
Types of devices with embedded systems are almost too numerous to list.
Examples include cell phones, digital cameras, video cameras, calculators, microwave
ovens, home security systems, washing machines, lighting systems, thermostats,
printers, various automotive systems (e.g., transmission control, cruise
control, fuel injection, anti-lock brakes, and suspension systems), tennis rackets,
toothbrushes, and numerous types of sensors and actuators in automated systems.
Often, embedded systems are tightly coupled to their environment. This can
give rise to real-time constraints imposed by the need to interact with the environment.
Constraints, such as required speeds of motion, required precision of measurement,
and required time durations, dictate the timing of software operations. If
multiple activities must be managed simultaneously, this imposes more complex
real-time constraints.

## Slide 36: Figure 1.14
Notes: Figure 1.14 shows in general terms an embedded system organization. In addition
to the processor and memory, there are a number of elements that differ from
the typical desktop or laptop computer:
■ There may be a variety of interfaces that enable the system to measure, manipulate,
and otherwise interact with the external environment. Embedded systems
often interact (sense, manipulate, and communicate) with external world
through sensors and actuators and hence are typically reactive systems; a reactive
system is in continual interaction with the environment and executes at a
pace determined by that environment.
■ The human interface may be as simple as a flashing light or as complicated as
real-time robotic vision. In many cases, there is no human interface.
■ The diagnostic port may be used for diagnosing the system that is being
controlled—not just for diagnosing the computer.
■ Special-purpose field programmable (FPGA), application-specific
(ASIC), or even nondigital hardware may be used to increase performance or reliability.
■ Software often has a fixed function and is specific to the application.
■ Efficiency is of paramount importance for embedded systems. They are optimized
for energy, code size, execution time, weight and dimensions, and cost.
There are several noteworthy areas of similarity to general-
purpose computer systems as well:
■ Even with nominally fixed function software, the ability to field upgrade to fix
bugs, to improve security, and to add functionality, has become very important
for embedded system, and not just in consumer devices.
■ One comparatively recent development has been of embedded system platforms
that support a wide variety of apps. Good examples of this are smartphones
and audio/visual devices, such as smart TVs.

## Slide 37: The Internet of Things (IoT)
Term that refers to the expanding interconnection of smart devices, ranging from appliances to tiny sensors
Is primarily driven by deeply embedded devices
Generations of deployment culminating in the IoT:
  Information technology (IT)
    PCs, servers, routers, firewalls, and so on, bought as IT devices by enterprise IT people and primarily using wired connectivity
  Operational technology (OT)
    Machines/appliances with embedded IT built by non-IT companies, such as medical machinery, SCADA, process control, and kiosks, bought as appliances by enterprise OT people and primarily using wired connectivity
  Personal technology
    Smartphones, tablets, and eBook readers bought as IT devices by consumers exclusively using wireless connectivity and often multiple forms of wireless connectivity
  Sensor/actuator technology
    Single-purpose devices bought by consumers, IT, and OT people exclusively using wireless connectivity, generally of a single form, as part of larger systems
  It is the fourth generation that is usually thought of as the IoT and it is marked by the use of billions of embedded devices
Notes: It is worthwhile calling out separately one of the major drivers in the proliferation
of embedded systems. The Internet of things (IoT) is a term that refers to the
expanding interconnection of smart devices, ranging from appliances to tiny sensors.
A dominant theme is the embedding of short- range mobile transceivers into a wide
array of gadgets and everyday items, enabling new forms of communication between
people and things, and between things themselves. The Internet now supports the
interconnection of billions of industrial and personal objects, usually through cloud
systems. The objects deliver sensor information, act on their environment, and, in
some cases, modify themselves, to create overall management of a larger system, like
a factory or city.
The IoT is primarily driven by deeply embedded devices (defined below).
These devices are low-bandwidth, low-repetition data-capture, and low-bandwidth
data-usage appliances that communicate with each other and provide data via user
interfaces. Embedded appliances, such as high-resolution
video security cameras, video VoIP phones, and a handful of others, require high-bandwidth
streaming capabilities. Yet countless products simply require packets of data to be intermittently
delivered.
With reference to the end systems supported, the Internet has gone through
roughly four generations of deployment culminating in the IoT:
1. Information technology (IT) : PCs, servers, routers, firewalls, and so on, bought
as IT devices by enterprise IT people and primarily using wired connectivity
2. Operational technology (OT) : Machines/appliances with embedded IT built
by non-IT companies, such as medical machinery, SCADA (supervisory control
and data acquisition), process control, and kiosks, bought as appliances by
enterprise OT people and primarily using wired connectivity
3. Personal technology: Smartphones, tablets, and eBook readers bought as IT
devices by consumers (employees) exclusively using wireless connectivity and
often multiple forms of wireless connectivity
4. Sensor/actuator technology: Single-purpose devices bought by consumers, IT,
and OT people exclusively using wireless connectivity, generally of a single
form, as part of larger systems
It is the fourth generation that is usually thought of as the IoT, and it is marked
by the use of billions of embedded devices.

## Slide 38: Embedded Operating Systems
There are two general approaches to developing an embedded operating system (OS):
  Take an existing OS and adapt it for the embedded application
  Design and implement an OS intended solely for embedded use
Application Processors
versus
Dedicated Processors
Application processors
  Defined by the processor’s ability to execute complex operating systems
  General-purpose in nature
  An example is the smartphone – the embedded system is designed to support numerous apps and perform a wide variety of functions
Dedicated processor
  Is dedicated to one or a small number of specific tasks required by the host device
  Because such an embedded system is dedicated to a specific task or tasks, the processor and associated components can be engineered to reduce size and cost
Notes: There are two general approaches to developing an embedded operating system
(OS). The first approach is to take an existing OS and adapt it for the embedded
application. For example, there are embedded versions of Linux, Windows, and
Mac, as well as other commercial and proprietary operating systems specialized for
embedded systems. The other approach is to design and implement an OS intended
solely for embedded use. An example of the latter is TinyOS, widely used in wireless
sensor networks. This topic is explored in depth in [STAL18].
In this subsection, and the next two, we briefly introduce some terms commonly
found in the literature on embedded systems. Application processors are defined
by the processor’s ability to execute complex operating systems, such as Linux,
Android, and Chrome. Thus, the application processor is general-purpose in nature.
A good example of the use of an embedded application processor is the smartphone.
The embedded system is designed to support numerous apps and perform a wide
variety of functions.
Most embedded systems employ a dedicated processor , which, as the name
implies, is dedicated to one or a small number of specific tasks required by the host
device. Because such an embedded system is dedicated to a specific task or tasks,
the processor and associated components can be engineered to reduce size and cost.

## Slide 39: Figure 1.15
Notes: As we have seen, early microprocessor chips included registers, an ALU, and some
sort of control unit or instruction processing logic. As transistor density increased, it
became possible to increase the complexity of the instruction set architecture, and
ultimately to add memory and more than one processor. Contemporary microprocessor
chips, as shown in Figure 1.2, include multiple cores and a substantial amount
of cache memory.
A microcontroller chip makes a substantially different use of the logic space
available. Figure 1.15 shows in general terms the elements typically found on a microcontroller
chip. As shown, a microcontroller is a single chip that contains the processor,
non-volatile memory for the program (ROM), volatile memory for input and output
(RAM), a clock, and an I/O control unit. The processor portion of the microcontroller
has a much lower silicon area than other microprocessors and much higher energy efficiency.
We examine microcontroller organization in more detail in Section 1.7.
Also called a “computer on a chip,” billions of microcontroller units are
embedded each year in myriad products from toys to appliances to automobiles. For
example, a single vehicle can use 70 or more microcontrollers. Typically, especially
for the smaller, less expensive microcontrollers, they are used as dedicated processors
for specific tasks. For example, microcontrollers are heavily utilized in automation
processes. By providing simple reactions to input, they can control machinery,
turn fans on and off, open and close valves, and so forth. They are integral parts of
modern industrial technology and are among the most inexpensive ways to produce
machinery that can handle extremely complex functionalities.
Microcontrollers come in a range of physical sizes and processing power. Processors
range from 4-bit to 32-bit architectures. Microcontrollers tend to be much
slower than microprocessors, typically operating in the MHz range rather than the
GHz speeds of microprocessors. Another typical feature of a microcontroller is that
it does not provide for human interaction. The microcontroller is programmed for a
specific task, embedded in its device, and executes as and when required.

## Slide 40: Deeply Embedded Systems
Subset of embedded systems
Has a processor whose behavior is difficult to observe both by the programmer and the user
Uses a microcontroller rather than a microprocessor
Is not programmable once the program logic for the device has been burned into ROM
Has no interaction with a user
Dedicated, single-purpose devices that detect something in the environment, perform a basic level of processing, and then do something with the results
Often have wireless capability and appear in networked configurations, such as networks of sensors deployed over a large area
Typically have extreme resource constraints in terms of memory, processor size, time, and power consumption
Notes: We have, in this section, defined the concept of an embedded system. A subset of
embedded systems, and a quite numerous subset, is referred to as deeply embedded
systems . Although this term is widely used in the technical and commercial
literature, you will search the Internet in vain (or at least I did) for a straightforward
definition. Generally, we can say that a deeply embedded system has a processor
whose behavior is difficult to observe both by the programmer and the user.
A deeply embedded system uses a microcontroller rather than a microprocessor, is
not programmable once the program logic for the device has been burned into ROM
(read-only memory), and has no interaction with a user.
Deeply embedded systems are dedicated, single-purpose devices that detect something in the environment,
perform a basic level of processing, and then do
something with the results. Deeply embedded systems often have wireless capability
and appear in networked configurations, such as networks of sensors deployed
over a large area (e.g., factory, agricultural field). The Internet of things depends
heavily on deeply embedded systems. Typically, deeply embedded systems have
extreme resource constraints in terms of memory, processor size, time, and power
consumption.

## Slide 41: ARM
Refers to a processor architecture that has evolved from RISC design principles and is used in embedded systems
Family of RISC-based microprocessors and microcontrollers designed by ARM Holdings, Cambridge, England
Chips are high-speed processors that are known for their small die size and low power requirements
Probably the most widely used embedded processor architecture and indeed the most widely used processor architecture of any kind in the world
Acorn RISC Machine/Advanced RISC Machine
Notes: The ARM architecture refers to a processor architecture that has evolved from
RISC design principles and is used in embedded systems. Chapter 7 examines
RISC design principles in detail. In this section, we give a brief overview of the
ARM architecture.
ARM is a family of RISC-based
microprocessors and microcontrollers designed
by ARM Holdings, Cambridge, England. The company doesn’t make processors
but instead designs microprocessor and multicore architectures and licenses them
to manufacturers. ARM Holdings has two types of licensable products:
processors and processor architectures. For a processor architecture, the customer buys
the rights to design their own processor compliant with ARM’s architecture.
ARM chips are high-speed
processors that are known for their small die size
and low power requirements. They are widely used in smartphones and other handheld
devices, including game systems, as well as a large variety of consumer products.
ARM chips are the processors in Apple’s popular iPod and iPhone devices,
and are used in virtually all Android smartphones as well. ARM’s partners shipped
16.7 billion ARM-based chips in 2016. ARM is probably the most widely used
embedded processor architecture and indeed the most widely used processor architecture
of any kind in the world [VANC14].
The origins of ARM technology can be traced back to the British-based
Acorn Computers company. In the early 1980s, Acorn was awarded a contract by the British
Broadcasting Corporation (BBC) to develop a new microcomputer architecture
for the BBC Computer Literacy Project. The success of this contract enabled Acorn
to go on to develop the first commercial RISC processor, the Acorn RISC Machine
(ARM). The first version, ARM1, became operational in 1985 and was used for
internal research and development as well as being used as a coprocessor in the
BBC machine.
In this early stage, Acorn used the company VLSI Technology to do the actual
fabrication of the processor chips. VLSI was licensed to market the chip on its own
and had some success in getting other companies to use the ARM in their products,
particularly as an embedded processor.
The ARM design matched a growing commercial need for a high-performance,
Low-power-consumption, small-size, and low-cost
processor for embedded applications.
But further development was beyond the scope of Acorn’s capabilities.
Accordingly, a new company was organized, with Acorn, VLSI, and Apple Computer
as founding partners, known as ARM Ltd. The Acorn RISC Machine became
Advanced RISC Machines. ARM was acquired by Japanese telecommunications
company SoftBank Group in 2016.

## Slide 42: ARM Products
Cortex-A
Cortex-R
Cortex-M
Cortex-M0
Cortex-M0+
Cortex-M3
Cortex-M4
Cortex-M7
Cortex-M23
Cortex-M33
Notes: ARM Holdings licenses a number of specialized microprocessors and related technologies,
but the bulk of their product line is the Cortex family of microprocessor
architectures. There are three Cortex architectures, conveniently labeled with the
initials A, R, and M.
The Cortex-A series of processors are application processors, intended
for mobile devices such as smartphones and eBook readers, as well as consumer
devices such as digital TV and home gateways (e.g., DSL and cable Internet
modems). These processors run at higher clock frequency (over 1 GHz), and
support a memory management unit (MMU), which is required for full feature OSs
such as Linux, Android, MS Windows, and mobile OSs. An MMU is a hardware
module that supports virtual memory and paging by translating virtual addresses
into physical addresses; this topic is explored in Chapter 8.
The two architectures use both the ARM and Thumb-2 instruction. Some of
the processors in this series are 32-bit machines and others are 64-bit machines.
The two architectures use both the ARM and Thumb-2
instruction sets; the principal difference is that the Cortex-A
is a 32-bit machine, and the Cortex-A50 is a 64-bit machine.
The Cortex-R is designed to support real-time applications, in which the
timing of events needs to be controlled with rapid response to events. They can run
at a fairly high clock frequency (e.g., 2 MHz to 4 MHz) and have very low response
latency. The Cortex-R includes enhancements both to the instruction set and to the
processor organization to support deeply embedded real-time devices. Most of these
processors do not have MMU; the limited data requirements and the limited number
of simultaneous processes eliminates the need for elaborate hardware and software
support for virtual memory. The Cortex-R does have a Memory Protection Unit
(MPU), cache, and other memory features designed for industrial applications. An
MPU is a hardware module that prohibits one program in memory from accidentally
accessing memory assigned to another active program. Using various methods,
a protective boundary is created around the program, and instructions within the
program are prohibited from referencing data outside of that boundary.
Examples of embedded systems that would use the Cortex-R are automotive
braking systems, mass storage controllers, and networking and printing devices.
Cortex-M series processors have been developed primarily for the
microcontroller domain where the need for fast, highly deterministic interrupt
management is coupled with the desire for extremely low gate count and
lowest possible power consumption. As with the Cortex-R
series, the Cortex-M architecture has an MPU but no MMU. The Cortex-M
uses only the Thumb-2 instruction set. The market for the Cortex-M
includes IoT devices, wireless sensor/actuator networks used in factories and other enterprises, automotive
body electronics, and so on.
There are currently seven versions of the Cortex-M series:
■ Cortex-M0 :
Designed for 8- and 16-bit applications, this model emphasizes low
cost, ultra low power, and simplicity. It is optimized for small silicon die size
(starting from 12k gates) and use in the lowest cost chips.
■ Cortex-M0+ :
An enhanced version of the M0 that is more energy efficient.
■ Cortex-M3 :
Designed for 16- and 32-bit applications, this model emphasizes
performance and energy efficiency. It also has comprehensive debug and trace
features to enable software developers to develop their applications quickly.
■ Cortex-M4 :
This model provides all the features of the Cortex-M3,
with additional instructions to support digital signal processing tasks.
■ Cortex-M7: Provides higher performance than the M4. It is still primarily a
32-bit machine but uses 64-bit wide instruction and data buses.
■ Cortex-M23: This model is similar to the M0+, and adds integer divide instructions
and some security features.
■ Cortex-M33: This model is similar to the M4, and adds some security features.
In this text, we will primarily use the ARM Cortex-M3 as our example embedded
system processor. It is the best suited of all ARM models for general-purpose
microcontroller use. The Cortex-M3 is used by a variety of manufacturers of microcontroller
products. Initial microcontroller devices from lead partners already
combine the Cortex-M3 processor with flash, SRAM, and multiple peripherals to
provide a competitive offering at the price of just $1.

## Slide 43: Figure 1.16
Notes: Figure 1.16 provides a block diagram of the EFM32 microcontroller from Silicon
Labs. The figure also shows detail of the Cortex-M3
processor and core components. We examine each level in turn.
The Cortex-M3 core makes use of separate buses for instructions and data.
This arrangement is sometimes referred to as a Harvard architecture, in contrast
with the von Neumann architecture, which uses the same signal buses and memory
for both instructions and data. By being able to read both an instruction and
data from memory at the same time, the Cortex-M3 processor can perform many
operations in parallel, speeding application execution. The core contains a decoder
for Thumb instructions, an advanced ALU with support for hardware multiply and
divide, control logic, and interfaces to the other components of the processor. In
particular, there is an interface to the nested vector interrupt controller (NVIC) and
the embedded trace macrocell (ETM) module.
The core is part of a module called the Cortex-M3 processor .
This term is somewhat misleading, because typically in the literature, the terms core and processor
are viewed as equivalent. In addition to the core, the processor includes the
following elements:
■ INVC : Provides configurable interrupt handling abilities to the processor. It
facilitates low-latency exception and interrupt handling, and controls power
management.
■ ETM : An optional debug component that enables reconstruction of program
execution. The ETM is designed to be a high-speed, low-power debug tool
that only supports instruction trace.
■ Debug access port (DAP) : This provides an interface for external debug
access to the processor.
■ Debug logic : Basic debug functionality includes processor halt, single-
step, processor core register access, unlimited software breakpoints, and full system
memory access.
■ ICode interface : Fetches instructions from the code memory space.
■ SRAM & peripheral interface : Read/write interface to data memory and peripheral
devices.
■ Bus matrix : Connects the core and debug interfaces to external buses on the
microcontroller.
■ Memory protection unit : Protects critical data used by the operating system
from user applications, separating processing tasks by disallowing access
to each other’s data, disabling access to memory regions, allowing memory
regions to be defined as read-only, and detecting unexpected memory accesses
that could potentially break the system.
The upper part of Figure 1.16 shows the block diagram of a typical microcontroller
built with the Cortex-M3, in this case the EFM32 microcontroller. This
microcontroller is marketed for use in a wide variety of devices, including energy,
gas, and water metering; alarm and security systems; industrial automation devices;
home automation devices; smart accessories; and health and fitness devices. The silicon
chip consists of 10 main areas:
■ Core and memory: This region includes the Cortex-M3
processor, static RAM (SRAM) data memory, and flash memory15 for storing program instructions
and nonvarying application data. Flash memory is nonvolatile (data is not lost
when power is shut off) and so is ideal for this purpose. The SRAM stores
variable data. This area also includes a debug interface, which makes it easy to
reprogram and update the system in the field.
■ Parallel I/O ports: Configurable for a variety of parallel I/O schemes.
■ Serial interfaces: Supports various serial I/O schemes.
■ Analog interfaces : Analog-to-digital and digital-to-analog
logic to support sensors and actuators.
■ Timers and triggers : Keeps track of timing and counts events, generates output
waveforms, and triggers timed actions in other peripherals.
■ Clock management : Controls the clocks and oscillators on the chip. Multiple
clocks and oscillators are used to minimize power consumption and provide
short startup times.
■ Energy management : Manages the various low-energy
modes of operation of the processor and peripherals to provide real-time
management of the energy needs so as to minimize energy consumption.
■ Security : The chip includes a hardware implementation of the Advanced
Encryption Standard (AES).
■ 32-bit bus : Connects all of the components on the chip.
■ Peripheral bus : A network which lets the different peripheral module communicate
directly with each other without involving the processor. This supports
timing-critical operation and reduces software overhead.
Comparing Figure 1.16 with Figure 1.2, you will see many similarities and
the same general hierarchical structure. Note, however, that the top level of a
microcontroller computer system is a single chip, whereas for a multicore computer,
the top level is a motherboard containing a number of chips. Another noteworthy
difference is that there is no cache, neither in the Cortex-M3 processor
nor in the microcontroller as a whole, which plays an important role if the code or
data resides in external memory. Though the number of cycles to read the instruction
or data varies depending on cache hit or miss, the cache greatly improves the
performance when external memory is used. Such overhead is not needed for a
microcontroller.

## Slide 44: Summary
Chapter 1
Organization and architecture
Structure and function
The IAS computer
Gates, memory cells, chips, and multichip modules
  Gates and memory cells
  Transistors
  Microelectronic chips
  Multichip module
The evolution of the Intel x86 architecture
Basic Concepts and Computer Evolution
Embedded systems
  The Internet of things
  Embedded operating systems
  Application processors versus dedicated processors
  Microprocessors versus microcontrollers
  Embedded versus deeply embedded systems
ARM architecture
  ARM evolution
  Instruction set architecture
  ARM products
Notes: Chapter 1 summary.

## Slide 45: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructions in teaching their courses and assessing student learning. dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permit- ted. The work and materials from it should never be made available to
students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these
restrictions and to honor the intended pedagogical purposes and the needs of
other instructors who rely on these materials.